# Introduction
This document defines and describes a command-oriented protocol for interaction with the SUNSET framework. The syntax defined herein is applicable to resource constrained computational systems such as the ones used in autonomous vehicles. However, the semantics of the commands can be used with different data formats, such as XML.

# Arguments Types
Commands are sequences of arguments and each argument has an associated type. The following subsections describe all the valid types.
### Integer
A number written without a fractional component.
### Real
A real number.
### String
A sequence of characters with arbitrary length.
### ParamName
Name of a SUNSET internal parameter.
- NODE_ID: Network identifier of the local node.
- BROADCAST_ID: Network identifier of the broadcast address.
- TX_POWER: Transmission power level of the acoustic modem.
### Position
Type describing the position of a system in the world.
Name	Type	Description
Latitude	Real	WGS-84 latitude in decimal degrees.
Longitude	Real	WGS-84 longitude in decimal degrees.
Depth	Real	Depth in meters. Negative values denote invalid or unknown depths.
Altitude	Real	Altitude in meters. Negative values denote invalid or unknown altitudes.

### ZUnits
Z value units.
- DEPTH: Z value represents depth.
- ALTITUDE: Z value represents altitude.
### ZReference
Z reference.
Name	Type	Description
Z Units	ZUnits	Z Units
Z Reference	Real	Z Reference

### SpeedUnits
Speed units.
- METER_PS: Speed is in m/s.
- RPM: Speed is in Rotations per Minute.
- PERCENTAGE: Speed is in percentage.
### SpeedReference
Speed reference.
Name	Type	Description
Speed Units	SpeedUnits	Speed Units
Speed Reference	Real	Speed Reference

### SensorInfoTuple
Sensor info tuple.
Name	Type	Description
Sensor Id	Integer	Sensor Id
Sensor Vendor	String	Speed Reference
Sensor Model	String	Speed Reference

### ManeuverGoto
A "Goto" is a maneuver specifying a movement of the vehicle to a target waypoint. The waypoint is described by the WGS-84 waypoint coordinate and target Z reference.
Name	Type	Description
Maneuver	String	Maneuver name. This argument has a fixed value of Goto.
Latitude	Real	WGS-84 Latitude of target waypoint in decimal degrees.
Longitude	Real	WGS-84 Longitude of target waypoint in decimal degrees.
Timeout	Integer	The amount of time the maneuver is allowed to run in seconds.
Z Reference	ZReference	Desired Z.
Speed Reference	SpeedReference	Desired Z.

### ManeuverStationKeeping
The Station Keeping maneuver makes the vehicle come to the surface and then enter a given circular perimeter around a waypoint coordinate for a certain amount of time.
Name	Type	Description
Maneuver	String	Maneuver name. This argument has a fixed value of StationKeeping.
Latitude	Real	WGS-84 Latitude of target waypoint in decimal degrees.
Longitude	Real	WGS-84 Longitude of target waypoint in decimal degrees.
Z Reference	ZReference	Desired Z.
Speed Reference	SpeedReference	Desired Z.
Radius	Real	Radius of the maneuver.
Duration	Integer	Maneuver duration. For unlimited duration use 0.

# Command Structure
## Header
Header format.
Name	Type	Description
Prefix	String	Synchronization field of all SUNSET commands. This argument has a fixed value of SSC.
Version	Integer	This field conveys the version of the command.
Flags	Integer
Time-to-live	Integer	The number of seconds, after which the command will expire if not successfuly acted upon.
Priority	Integer	The priority of the command. The higher the number the higher the priority.
Source	Integer	Source node identifier.
Destinations Count	Integer	Number of destination addresses in the Destinations field.
Destinations	List of Integer	List of identifiers of destination nodes.
Command Name	String	Name of the command.

## Footer
Footer.
Name	Type	Description
CRC16	Integer	CRC-16-IBM of all preceding octects. The polynomial used is x^16 + x^15 + x^2 + 1 (0x8005)
Terminator	String	Command terminator. This argument has a fixed value of \n.

# General Commands
General Commands.
## CommandOk
This command shall be sent immediately in response to a command that was received, decoded and correctly interpreted.
### Arguments
Name	Type	Description
Name	String	Name of the received command.

## CommandError
This command shall be sent immediately in response to a command that could not be interpreted or fulfilled.
### Arguments
Name	Type	Description
Error	String	This field conveys the reason for the error. / INVALID_CRC: The CRC of the command is not present or is invalid. / INVALID_FORMAT: The command has an invalid format. / INVALID_VERSION: The command has a version that it not supported. / INVALID_REQUEST: The command contained an invalid request. / INVALID_VALUE: The command contained an invalid value. / BUSY: The command cannot be fulfilled at the present time.

## CommandFailure
This command shall be sent asynchronously when a command that was previously accepted fails permanently in an unrecoverable way.
### Arguments
Name	Type	Description
Error	String	This field conveys the reason for the failure. / INVALID_VERSION: The command has a version that it not supported by the remote node. / INVALID_REQUEST: The command contained a request that was considered invalid by the remote node. / EXPIRED: The command's time-to-live was reached. / INTERNAL_ERROR: The system cannot execute the command for some internal problem.
Sequence Number	Integer	A non-negative number conveying the unique sequence number of the request. The number -1 means no sequence number was issued for this particular command (e.g., local request). The sequence number will wrap around at an unspecified number. However, SUNSET shall guarantee that all requests currently being processed will have unique sequence numbers.

# Low-level Commands
Low-level commands.
## PacketTx
This command requests transmission of a packet with user-defined data. Upon reception SUNSET shall reply with a PacketTxStatus with a RECEIVED Status Code.
### Arguments
Name	Type	Description
Data Length	Integer	Number of characters of the Data field.
Data	String	Hexadecimal coded data octets. Two upper case characters per octet (00-FF).

## PacketTxStatus
This command conveys the status of a transmission request. It shall be sent in reply to a PacketTx command or asynchronously in the case of unsolicited SUNRISE internal transmissions.
### Arguments
Name	Type	Description
Sequence Number	Integer	A non-negative number conveying the unique sequence number of the request. The number -1 means no sequence number was issued for this particular command (e.g., local request). The sequence number will wrap around at an unspecified number. However, SUNSET shall guarantee that all requests currently being processed will have unique sequence numbers.
Status	String	Status of the transmission request. / RECEIVED: The transmission request was received and is being processed. / ERROR: An error has occurred while processing the transmission. See field Error Code for more information. / QUEUED: The transmission request has been queued and is waiting to be transmitted. / TX_START: Transmission of the request has started. In cases where the request is broken down into several modem frames several PacketTxStatus messages with this Status Code shall be sent, one for each frame. / TX_END: Transmission of the request has ended. The remarks of START_TX also apply to this status code. / TRANSMITTED: Packet was successfully transmitted in its entirety. / DELIVERED: Packet was received in its entirety by the destination nodes. / EXPIRED: The time-to-live of the transmission request was reached, and the packet was not transmitted or delivered in its entirety. / CANCELED: The packet transmission request was canceled.
Error	String	Error type. / SUCCESS: No error has occurred. / TX_RETRY_LIMIT: Maximum number of transmission retries was reached.

## PacketRx
Notification of packet reception.
### Arguments
Name	Type	Description
Data Length	Integer	Number of characters of the Data field.
Data	String	Hexadecimal coded data octets. Two upper case characters per octet (00-FF).

## Param
The Param command shall be dispatched in response to a ParamGet or ParamSet commands in response to a get or set command.
### Arguments
Name	Type	Description
Name	ParamName	The name of the setting/parameter to get.
Value	String	The value for the requested setting. The format of the value depends on the target setting. See Table X for a description of valid parameters.

## ParamGet
The UamParamGet command shall instruct the destination system(s) to return the value for the given setting (parameter). Upon reception and interpretation, each destination system shall reply with a UamParam command.
### Arguments
Name	Type	Description
Name	ParamName	The name of the setting/parameter to get.

## ParamSet
The UamParamSet command shall instruct the destination system(s) to set the target parameter with the given value. Upon reception and interpretation, each destination system shall reply with a UamParam command.
### Arguments
Name	Type	Description
Name	ParamName	The name of the setting/parameter to get.
Value	String	The value for the requested setting. The format of the value depends on the target setting. See Table X for a description of valid parameters.

# Plan Management
Plan management commands.
## Abort
The Abort command shall instruct the destination system(s) to cancel any type of automatic control and enter standby mode. Upon reception and interpretation, each destination system shall reply with an Aborted command.
### Arguments
This command has no arguments.
## Aborted
The Aborted command shall be dispatched in response to an Abort command.
### Arguments
This command has no arguments.
## PlanListGet
The PlanListGet command shall instruct the destination system(s) to return the list of plans that can be executed on the target system(s). Upon reception and interpretation, each destination system shall reply with a PlanList command.
### Arguments
This command has no arguments.
## PlanList
The PlanList command shall be dispatched in response to a PlanListGet command.
### Arguments
Name	Type	Description
Plan Count	Integer	Number of plans available on the system.
Plan Names	List of String	List of available plan names.

## PlanGet
The PlanGet command shall instruct the destination system(s) to return the list of maneuvers for the requested plan. Upon reception and interpretation, each destination system shall reply with a Plan command.
### Arguments
Name	Type	Description
Plan Name	String	Name of the desired plan.

## Plan
The Plan command shall be dispatched in response to a PlanGet command.
### Arguments
Name	Type	Description
Maneuver Count	Integer	Number of maneuvers for the requested plan. It is 0 if the requested plan is not a valid plan (not available on the system or with no maneuvers).
Maneuver List	List of: / ManeuverGoto / ManeuverStationKeeping	List of the maneuvers of the plan.

## PlanStart
The PlanStart command shall instruct the destination system(s) to start the requested plan. Upon reception and interpretation, each destination system shall reply with a PlanStarted command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the plan to start.

## PlanStarted
The PlanStarted command shall be dispatched in response to a PlanStart command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the started plan.

## PlanStop
The PlanStop command shall instruct the destination system(s) to stop the plan currently running on the vehicle. Upon reception and interpretation, each destination system shall reply with a PlanStopped command.
### Arguments
This command has no arguments.
## PlanStopped
The PlanStopped command shall be dispatched in response to a PlanStop command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the plan that was stopped.

## PlanDelete
The PlanDelete command shall instruct the destination system(s) to delete the requested plan. Upon reception and interpretation, each destination system shall reply with a PlanDeleted command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the plan to delete.

## PlanDeleted
The PlanDeleted command shall be dispatched in response to a PlanDelete command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the deleted plan.

## PlanAdd
The PlanAdd command shall instruct the destination system(s) to add the requested plan. Upon reception and interpretation, each destination system shall reply with a PlanAdded command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the plan to add.
Maneuver Count	Integer	Number of maneuvers in the plan.
Maneuver List	List of: / ManeuverGoto / ManeuverStationKeeping	The maneuvers of the new plan.

## PlanAdded
The PlanAdded command shall be dispatched in response to a PlanAdd command.
### Arguments
Name	Type	Description
Plan Name	String	The name of the plan added to the system.

# Sensor Management
Sensor management commands.
## SensorListGet
The SensorListGet command shall instruct the destination system(s) to return the list of measurements available at the target system(s). Multiple sensors can be available returning the same measurement. Upon reception and interpretation, each destination system shall reply with a SensorList command.
### Arguments
This command has no arguments.
## SensorList
The SensorList command shall be dispatched in response to a SensorListGet command.
### Arguments
Name	Type	Description
Measurement Count	Integer	Number of measurements available at the target system.
Measurement Names	List of String	Name of the available measurements.

## SensorInfoGet
The SensorInfoGet command shall instruct the destination system(s) to return the list of sensors for the requested measurement. Upon reception and interpretation, each destination system shall reply with a SensorInfo command.
### Arguments
Name	Type	Description
Measurement Name	String	The name of the desired measurement.

## SensorInfo
The SensorInfo command shall be dispatched in response to a SensorInfoGet command.
### Arguments
Name	Type	Description
Measurement Name	String	The name of the desired measurement.

## SensorSampleGet
The SensorSampleGet command shall instruct the destination system(s) to return the measurement for the target of sensor. Upon reception and interpretation, each destination system shall reply with a SensorSample command.
### Arguments
Name	Type	Description
Measurement Name	String	The name of the desired measurement.
Sensor Identifier	Integer	The sensor identifier, 0 is for the default sensor.
Sampling Frequency	Real	Sampling frequency. If Hz is 0, single shot.

## SensorSample
The SensorSample command shall be dispatched in response to a SensorSampleGet command.
### Arguments
Name	Type	Description
Position	Position	Position where sample was collected.
Measurement Name	String	The name of the target measurement.
Sensor Identifier	Integer	The sensor identifier, 0 is for the default sensor.
Sample	Real	The sample for the requested sensor. Its format depends on the target sensor and measurement.

# Position and Ranging
Position and ranging commands.
## PositionGet
The PositionGet command shall instruct the destination systems to return their position in the world. Upon reception and interpretation, each destination system shall reply with a Position command.
### Arguments
Name	Type	Description
Frequency	Real	Update frequency in Hertz. If this field is 0 then a single position update will be requested.

## Position
The Position command shall be dispatched in response to a PositionGet command or asynchronously every time such estimation is available.
### Arguments
Name	Type	Description
Value	Position
Heading	Real	Heading in degrees.

## RangeGet
The RangeGet command shall instruct the destination system(s) to return the estimated range to the target system(s). Upon reception and interpretation, each destination system shall reply with a Range command.
### Arguments
Name	Type	Description
Target Count	Integer	Number of target addresses.
Targets	List of Integer	Number of target addresses.
Frequency	Real	Range estimation frequency. If Hz is 0, single shot.

## Range
The Range command shall be dispatched in response to a RangeGet command or in an asychronous way every time such estimation is available.
### Arguments
Name	Type	Description
Target	Integer	Target address.
Travel Time	Real	Estimated travel time to the target node in seconds.
Bearing	Real	Estimated bearing angle to the target node in degrees.